# Clock Time
The RPI does not include clock hardware. On loss of power, it can loose time, such that clock is wrong on reboot.
Pi is configured to synch to NTP server, using ntpd program. Settings are in /etc/ntp.conf
The protocol prevents update of the clock if the difference between the current clock setting and the NTP time is greater than 1000s (17 minutes).
PI will normally 'remember' time when it was shutdown, and on start-up, resume from that time. The clock will therefore be slow when it reboots until such time as it re-synchronises. If unit was down for more than 1000s then clock will be sufficiently slow that it exceeds the 1000s limit, and thus will not synchronise to NTP.
To reset the clock we can override the 1000s limit by running ntpd from shell with swith -g and with switch -q to exit once done.
I found this was only effective after stopping the ntp service. Hence, shell commands to execute are:
sudo /etc/init.d/ntp stop
sudo ntpd -q-g
sudo /etc/init.d/ntp start
or run script sh Myscripts/fix_time.sh
shell command nptq will give actual data about ntp server results, including offset from clock time in ms.
This can be obtained in python with:
subprocess.Popen(['ntpq', '-p'], stdout=subprocess.PIPE).communicate()[0]
Take's a bit of parsing, though. There is a script for that here: http://www.ridgesolutions.ie/index.php/2015/04/29/python-script-to-query-ntp-status-and-return-it-as-json/